## Slide 1
IO Handler
  Handles all communication between GFAU and external device
  Asynchronous parallel protocol and scalable IO bus make communication fast and flexible
  Figure 3: Timing Diagram
Memory wrapper
  Handle memory read and write requests from the generator, operators and control unit
What are Galois Fields?
Galois fields (pronounced “Gal-o-AH”), or fields with a finite field order, are a key part of number theory, abstract algebra, arithmetic algebraic geometry, and cryptography. In error detection and correction. Galois fields are utilized in cyclic redundancy check (CRC) which are used in digital networks and storage devices to detect accidental changes to raw data.
Table 1: Elements of GF[x](23) = x3 + x2 + x0
Figure 1: Example Operations in GF[x](23)
Objective
To design a scalable arithmetic logic unit (ALU) capable of generating elements in the Galois field of an irreducible polynomial and perform addition, subtraction, multiplication, division and logarithm for low powered devices.
Design Approach
Scalable, parameterized and efficient design prioritized over specific platform hardware requirements
Designed entirely in VHSIC Hardware Description Language (VHDL) modules and packages
Capability of design limited only by external memory capacity
Interface <BRIAN>
Design Overview
Figure 3: Functional Flow Diagram
Element | Symbol | Polynomial | Symbol
0 | NULL | 0 + 0 + 0 | 000
x0 | 000 | 0 + 0 + x0 | 001
x1 | 001 | 0 + x1 + 0 | 010
x2 | 010 | x2 + 0 + 0 | 100
x3 | 011 | x2 + 0 + x0 | 101
x4 | 100 | x2 + x1 + x0 | 111
x5 | 101 | 0 + x1 + x0 | 011
x6 | 110 | x2 + x1 + 0 | 110
Modules
Global Registers
  Generated by priority encoders
  Size index, most significant bit index, and mask
Generator
  Generates elements in their element and polynomial forms
  Alerts the user when process is complete
Operators
  Performs addition, subtraction, multiplication, division and logarithm of Galois operands
  Checks null errors
Control unit
  Determines operations requested through 6-bit opcode
  Converts operands into their counterpart forms if necessary
  Checks operand memberships and null operands
Galois Field Arithmetic Unit (GFAU)
Sabbir Ahmed, Jeffrey Osazuwa, Howard To, Brian Weber, Dr. E.F. Charles LaBerge
Department of Computer Science and Electrical Engineering, University of Maryland, Baltimore County
Figure x: GFAU Block Schematic
Results
Conclusions